## Slide 1: There are relatively few engines using a wet-sump type of oil system.
Relatively few engines use a wet-sump oil system.

## Slide 2: A schematic diagram of a wet-sump oil system is shown in Figure 6-47.
Figure 6-47 shows a schematic diagram of a wet-sump oil system.

## Slide 3: A magnetic drain plug may be provided to drain the oil and also to trap any ferrous metal particles in the oil.
Some manufacturers provide a magnetic drain plug to drain the oil and trap ferrous metal particles.

## Slide 4: This plug should always be examined closely during inspections.
Always examine this plug closely during inspection.

## Slide 5: This system is typical of all engines using a wet-sump lubrication system.
This system is typical of all engines that use a wet-sump lubrication system.

## Slide 6: The oil is returned to the reservoir (sump) by gravity.
Trough gravity the oil returns to the reservoir (sump).

## Slide 7: Maintenance of gas turbine lubrication systems consists mainly of adjusting, removing, cleaning, and replacing various components.
You must adjust, remove, clean and replace various components to maintain an gas turbine lubrication system.
During maintenance you must adjust, remove, clean and replace various components of the gas turbine lubrication system.

## Slide 8: Oil filter maintenance and oil change intervals for turbine engines vary widely from model to model, depending on the severity of the oil temperature conditions imposed by the specific airframe installation and engine configuration.
The oil filter maintenance and the oil change intervals for turbine engines vary widely from model to model. The intervals depend on the severity of the oil temperature conditions. These are a result of the specific airframe installation and engine configuration.

## Slide 9: The applicable manufacturer’s instructions should be followed.
Follow the applicable manufacturer’s instructions.

## Slide 10: The oil filter should be removed at every regular inspection.
We recommend to remove the oil filter at every regular inspection.

## Slide 11: It should be disassembled, cleaned, and any worn or damaged filter elements replaced.
Disassemble and clean the oil filter. Replace any worn or damaged filter elements.

## Slide 12: Provide a suitable container for collecting the drained oil, if needed.
Provide a suitable container, which is able to (can) collect the drained oil, if needed.
Provide a suitable container to collect the drained oil.
If you drain the oil, use a suitable container to collect it.

## Slide 13: Remove the filter housing and withdraw the filter assembly. [Figure 6-48] Discard the old seals.

## Slide 14: Rinse them in a degreaser fluid or cleaning solvent.

## Slide 15: Then, install the filter in the filter housing assembly.